## Slide 1
Vehicle
Edge node
Edge pod #1
Redis Database
On Board Unit(OBU)
Kubernetes
Prometheus
Dashboard (Grafana)
Core
Kubeflow
Kepler
Ingress
Operator
(user)
Edge pod #2
Kserve
inference service
Minio Storage
Jupyter notebook
energy, CPU,
memory usage stats
Kserve
model serving
Architecture Overview

## Slide 2
Architecture Overview – Networking – Vehicle data processing
Vehicle sends measurements to Vehicle API service (provided by Idneo – data preprocessing +Redis DB)
  transmission is received by antenna
  Transmission enters data(IPv4/IPv6) network
  Data is forwarded to the closest Kubernetes Edge node using (i) Anycast IP address, shared by all Edge Nodes, and (ii) nodePort defined in NodePort service
  Edge Node receives the data, checks the IP table in kube-proxy, and forwards it to local Pod A as the service is configured with `externalTrafficPolicy: Local`
    If there is no local Pod for Vehicle API service, the packet is dropped
Vehicle API service forwards the data to the ML prediction service(Kserve inference)
  Data is forwarded to Pod B as Kserve inference service is configured with `internalTrafficPolicy: Local`
    If there is no local Pod for Kserve inference service, the packet is dropped
  or ML prediction service pod periodically queries local Redis DB in Vehicle API service – as Vehicle API service is also configured with `internalTrafficPolicy: Local`
    If there is no local Pod for Vehicle API service, the queries/requests are dropped
Kserve inference service pushes the data into Prometheus
Grafana periodically queries data from Prometheus
Vehicle
On Board Unit(OBU)
Edge Node #1
Vehicle API
Pod A
Kserve inference
Pod B
kube-proxy
Antenna
(5G network)
Data Network
(IPv4/IPv6)
AnycastIP:nodePort
IF(e.g. Eth0)
IP address
Anycast address
Edge Node #2
Vehicle API
Pod C
Kserve inference
Pod D
kube-proxy
IF(e.g. Eth0)
IP address
Anycast address
Core Node/Nodes
kube-proxy
IF(e.g. Eth0)
IP address
…
Prometheus
Dashboard
(Grafana)
Kubeflow w Jupyter NB
Kepler
ingress
Minio Storage
Kserve
Service name | Service type | Note
Vehicle API | NodePort | externalTrafficPolicy: Local internalTrafficPolicy: Local Externally Accessible through Anycast/NodeIP:nodePort
Kserve Inference | ClusterIP | internalTrafficPolicy: Local
Kepler | ClusterIP | 
Prometheus | ClusterIP | 
Kserve | ClusterIP | 
Kubeflow | ClusterIP | GUI accessible through Ingress
Minio Storage | ClusterIP | 
Grafana | ClusterIP | GUI accessible through Ingress
services
1
3
2
User
Data Network
(IPv4/IPv6)
FQDN
4

## Slide 3
Architecture Overview – Networking – Energy consumption monitoring
Kepler exporter uses eBPF to probe CPU, GPU, RAM performance counters and exposes them over time via HTTP
Prometheus periodically queries Kepler exporter for a new data
Grafana periodically queries Prometheus for anew data
Vehicle
On Board Unit(OBU)
Edge Node #1
Vehicle API
Pod A
Kserve inference
Pod B
kube-proxy
Antenna
(5G network)
Data Network
(IPv4/IPv6)
AnycastIP:nodePort
IF(e.g. Eth0)
IP address
Anycast address
Edge Node #2
Vehicle API
Pod C
Kserve inference
Pod D
kube-proxy
IF(e.g. Eth0)
IP address
Anycast address
Core Node/Nodes
kube-proxy
IF(e.g. Eth0)
IP address
…
Prometheus
Dashboard
(Grafana)
Kubeflow w Jupyter NB
Kepler
ingress
Minio Storage
Kserve
Service name | Service type | Note
Vehicle API | NodePort | externalTrafficPolicy: Local Externally Accessible through Anycast/NodeIP:nodePort
Kserve Inference | ClusterIP | internalTrafficPolicy: Local
Kepler | ClusterIP | 
Prometheus | ClusterIP | 
Kserve | ClusterIP | 
Kubeflow | ClusterIP | GUI accessible through Ingress
Minio Storage | ClusterIP | 
Grafana | ClusterIP | GUI accessible through Ingress
services
User
Data Network
(IPv4/IPv6)
FQDN
1
3
2

## Slide 4
Architecture Overview – Networking – Vehicle data and energy consumption monitoring
User enters Grafana FQDN in the web browser and is forwarded to the Ingress controller
Ingress controller translates the FQDN to the appropriate service and forwards it
Grafana GUI comes up in the Users web browser
Vehicle
On Board Unit(OBU)
Edge Node #1
Vehicle API
Pod A
Kserve inference
Pod B
kube-proxy
Antenna
(5G network)
Data Network
(IPv4/IPv6)
AnycastIP:nodePort
IF(e.g. Eth0)
IP address
Anycast address
Edge Node #2
Vehicle API
Pod C
Kserve inference
Pod D
kube-proxy
IF(e.g. Eth0)
IP address
Anycast address
Core Node/Nodes
kube-proxy
IF(e.g. Eth0)
IP address
…
Prometheus
Dashboard
(Grafana)
Kubeflow w Jupyter NB
Kepler
ingress
Minio Storage
Kserve
Service name | Service type | Note
Vehicle API | NodePort | externalTrafficPolicy: Local Externally Accessible through Anycast/NodeIP:nodePort
Kserve Inference | ClusterIP | internalTrafficPolicy: Local
Kepler | ClusterIP | 
Prometheus | ClusterIP | 
Kserve | ClusterIP | 
Kubeflow | ClusterIP | GUI accessible through Ingress
Minio Storage | ClusterIP | 
Grafana | ClusterIP | GUI accessible through Ingress
services
User
Data Network
(IPv4/IPv6)
FQDN, e.g: success6g.grafana.es
1
3
2

## Slide 5
Architecture Overview – Networking – ML model development/update
User enters Kubeflow FQDN in the web browser and is forwarded to the Ingress controller
Ingress controller translates the FQDN to the appropriate service and forwards it
Kubeflow GUI comes up in the Users web browser and user can spawn a Jupyter Notebook in the Kubeflow to develop a new ML inference model
Vehicle
On Board Unit(OBU)
Edge Node #1
Vehicle API
Pod A
Kserve inference
Pod B
kube-proxy
Antenna
(5G network)
Data Network
(IPv4/IPv6)
AnycastIP:nodePort
IF(e.g. Eth0)
IP address
Anycast address
Edge Node #2
Vehicle API
Pod C
Kserve inference
Pod D
kube-proxy
IF(e.g. Eth0)
IP address
Anycast address
Core Node/Nodes
kube-proxy
IF(e.g. Eth0)
IP address
…
Prometheus
Dashboard
(Grafana)
Kubeflow w Jupyter NB
Kepler
ingress
Minio Storage
Kserve
Service name | Service type | Note
Vehicle API | NodePort | externalTrafficPolicy: Local Externally Accessible through Anycast/NodeIP:nodePort
Kserve Inference | ClusterIP | internalTrafficPolicy: Local
Kepler | ClusterIP | 
Prometheus | ClusterIP | 
Kserve | ClusterIP | 
Kubeflow | ClusterIP | GUI accessible through Ingress
Minio Storage | ClusterIP | 
Grafana | ClusterIP | GUI accessible through Ingress
services
User
Data Network
(IPv4/IPv6)
FQDN, e.g: success6g.kubeflow.es
1
3
2

## Slide 6
Architecture Overview – Networking – ML model deployment
Kubeflow instructs Kserve to deploy a model
Kserve queries the model from Minio storage
Kserve updates/”serves” the model in all Kserver inference Pods
Vehicle
On Board Unit(OBU)
Edge Node #1
Vehicle API
Pod A
Kserve inference
Pod B
kube-proxy
Antenna
(5G network)
Data Network
(IPv4/IPv6)
AnycastIP:nodePort
IF(e.g. Eth0)
IP address
Anycast address
Edge Node #2
Vehicle API
Pod C
Kserve inference
Pod D
kube-proxy
IF(e.g. Eth0)
IP address
Anycast address
Core Node/Nodes
kube-proxy
IF(e.g. Eth0)
IP address
…
Prometheus
Dashboard
(Grafana)
Kubeflow w Jupyter NB
Kepler
ingress
Minio Storage
Kserve
Service name | Service type | Note
Vehicle API | NodePort | externalTrafficPolicy: Local Externally Accessible through Anycast/NodeIP:nodePort
Kserve Inference | ClusterIP | internalTrafficPolicy: Local
Kepler | ClusterIP | 
Prometheus | ClusterIP | 
Kserve | ClusterIP | 
Kubeflow | ClusterIP | GUI accessible through Ingress
Minio Storage | ClusterIP | 
Grafana | ClusterIP | GUI accessible through Ingress
services
User
Data Network
(IPv4/IPv6)
FQDN
1
3
2

## Slide 7
Real-world testing and data gathering - Parcmotor Castellolí
legend:
mandatory
Optional
steps:
prepare the Kserve model and helm charts
make testing requests before the day of testing
run the real-world test with vehicles in Castelloli
query and save Kepler stats (CPU,RAM usage + CO2 estimation) from Prometheus
query and save measurements and predictions from Prometheus
make screenshots: Grafana, NBC environment
make vehicle pictures
Vehicle
Edge node #1
Edge pod #1
Redis Database
On Board Unit(OBU)
Kubernetes
Prometheus
Dashboard (Grafana)
Core
Kepler
Ingress
Operator
(user)
Edge pod #2
Kserve
inference service
energy, CPU,
memory usage stats
Kserve
model serving
Edge node #2
Edge node #3

## Slide 8
Vehicle
Edge node #1
Edge pod #1
Redis Database
On Board Unit(OBU)
Kubernetes
Prometheus
Dashboard (Grafana)
Core
Kepler
Ingress
Operator
(user)
Edge pod #2
Kserve
inference service
energy, CPU,
memory usage stats
Kserve
model serving
Edge node #2
Edge node #3

## Slide 9
R&D – Testbed (SUPERCOM/Cloud)
steps:
setup full testbed
use RaspberryPis to emulate edge nodes
send gathered data using python script and target specific edge nodes (emulation of vehicle moving between base stations)
test centralized vs edge computation vs federated learning
query and save Kepler stats (CPU,RAM usage + CO2 estimation) from Prometheus
query and save measurements and predictions from Prometheus
make screenshots: Grafana, Testbed environment
make pictures of used HW (RaspberyPis, workstation, SUPERCOM servers rack?)
laptop
Edge node #1 (RaspberryPi)
Edge pod #1
Redis Database
Python script
Kubernetes
Prometheus
Dashboard (Grafana)
Core
Kubeflow
Kepler
Ingress
Operator
(user)
Edge pod #2
Kserve
inference service
Minio Storage
Jupyter notebook
energy, CPU,
memory usage stats
Kserve
model serving
Edge node #2
Edge node #3

## Slide 10
laptop
Edge node #1 (RaspberryPi)
Edge pod #1
Redis Database
Python script
Kubernetes
Prometheus
Dashboard (Grafana)
Core
Kubeflow
Kepler
Ingress
Operator
(user)
Edge pod #2
Kserve
inference service
Minio Storage
Jupyter notebook
energy, CPU,
memory usage stats
Kserve
model serving
Edge node #2
Edge node #3